## Slide 1
HydroGeoChem Explorer
Predicting how water chemistry behaves, so it stays safe on the way to the tap
A project overview for the team
For communities · utilities · farmers · regulators · researchers who depend on water
Notes: HydroGeoChem Explorer takes real water-quality measurements, converts them into the exact form the PHREEQC geochemistry program needs, runs it safely, and returns reproducible answers, plus tools to build machine-learning datasets across many sites.

## Slide 2
1
The problem we solve
Everyone who depends on water shares one question: will it stay safe on the way to the tap, clogging pipes with scale or eating through them and pulling in metals like lead?
The measurements
How much calcium, sulfate, chloride and so on is dissolved. Government agencies have published these free for decades.
The calculation, PHREEQC
A famous government program (since the 1980s) that predicts which minerals dissolve and which crystallise out.
Today the gap is manual
Someone downloads a spreadsheet, retypes numbers into PHREEQC's own text format, runs it, and reads the output. About twenty minutes per site, and it goes wrong in ways nobody notices.
Notes: The two ingredients exist and are free; connecting them is the manual, error-prone gap this system closes.

## Slide 3
2
The real product: the translator
Lab data does not arrive in the form the calculation needs. Getting it right is the whole point.
1000×
Iron reported in micrograms, calcium in milligrams. Mix them up and you overstate iron a thousandfold.
4.4×
Nitrate can be reported as the whole molecule or as just its nitrogen, a 4.4× difference.
1.22×
Alkalinity is quoted “as calcium carbonate,” which is 22% off from what is really in the water.
PHREEQC accepts the wrong number, finishes happily, and returns a confident answer that is nonsense. The translator knows every measurement's scale, convention, and PHREEQC name.
Notes: This is the single most important idea: the value is in correct unit and convention handling, not in running PHREEQC.

## Slide 4
3
What it does, end to end
1
Find
Locate sites that actually have the analytes you need.
2
Fetch & clean
Pull analyses and run them through the translator.
3
Preview
Show the exact PHREEQC input before running.
4
Run
Model safely; return saturation indices + charts.
5
Export
Join inputs and outputs into an ML-ready table.
The UI is a pure client of the API, what a scientist sees on screen is exactly what a script gets back.
Notes: Five capabilities, front to back. Find and Export are the two newer pieces; the middle three are the core modelling loop.

## Slide 5
4
The technology stack, in plain terms
Python
The language for all of it
FastAPI
The web service, the front desk
Streamlit
The interface scientists click
PHREEQC / phreeqpy
The geochemistry engine
PostgreSQL
Remembers every run + sample
Redis + Celery
Queue + workers for slow jobs
Docker
Bundles it to run anywhere
pandas
Builds the exported datasets
Nothing exotic, each choice maps to one specific job.
Notes: Standard, boring-on-purpose stack. The only specialist piece is PHREEQC/phreeqpy, the geochemistry engine.

## Slide 6
5
How it's organised: layers that point downward
hgc.ui
The screen, pure display, knows no chemistry
hgc.api
The front desk, checks who's asking, what to do
hgc.services
The machinery, data, engine, orchestration
hgc.db
The memory, the only part that speaks SQL
hgc.domain
The knowledge, units, conventions, sanity checks
depends on
Why seal off the chemistry?
It is the part that must never be wrong. Because it cannot touch the internet, the database, or PHREEQC, its correctness is checked in full with fast, simple tests, no network, no setup.
Notes: Dependency arrows point inward only. The domain (chemistry) imports nothing, which is what makes it completely testable.

## Slide 7
6
The hard part: running PHREEQC safely
One thing at a time
Two runs sharing one copy contaminate each other, plausible, wrong answers.
Cannot be interrupted
A badly-conditioned model can loop forever, with no polite way to stop it.
Slow to wake up
Loading its thermodynamic reference tables takes a noticeable moment.
The fix: isolated booths
Give each calculation its own process, with a private copy of PHREEQC and its tables kept warm. If a booth locks up, we don't reason with it, we demolish it and build a new one. One bad model can never freeze the service for everyone else.
Golden rule: one booth per processor core, no more, oversubscribing turns a fast run into a timeout.
Notes: Process isolation, plus a hard rule about not running more workers than cores. Experts' raw input gets two independent locks (a text filter and an OS-level zero-file-write limit).

## Slide 8
7
Three habits that keep the science honest
1
Show the working
The exact PHREEQC input is available before and after every run. A result you can't inspect is one you can't defend in a report.
2
Check the books balance
Water is electrically neutral, so charges must cancel. The tool computes this for every sample and flags anything beyond 10%, a built-in lie detector.
3
Say when you don't know
“No data here” and “the service is down” are different messages. A silent wrong answer is the most dangerous bug in a scientific tool.
Notes: These three habits are what separate a trustworthy scientific tool from a black box that emits numbers.

## Slide 9
8
New: machine-learning datasets
One flat table, each row a sample, inputs joined with the model outputs.
id_*
site, date, coords
LABELS
in_*
analytes + charge balance
FEATURES
out_*
pH, pe, ionic strength
OUTPUTS
si_*
saturation index / mineral
TARGETS
meta_*
database + engine version
PROVENANCE
Sparse data, handled honestly
A single visit rarely measures the whole ion suite, so rows can aggregate per month, quarter, or year into one complete analysis.
Built from one site or many at once, search, multi-select, and download a combined dataset from the UI, or run the CLI across a whole state.
Notes: The dataset joins features and targets in one table. Bucketing (month/quarter/year) recombines sparse sampling events into complete, modelable rows.

## Slide 10
Five ideas to remember
1
The real product is the translator. Units and conventions, done right, not PHREEQC itself.
2
The chemistry is sealed off. So it can be tested completely, which drives the whole layering.
3
Each calculation runs in its own booth. Stability and safety over cleverness.
4
Every answer is reproducible. Tied to the exact data and software version that made it.
5
It is honest about uncertainty. Charge balance and named failures keep wrong answers out.
Run it
make install
make databases
make test
make api
make ui
localhost:8000 · 8501
The goal: safe, non-damaging water on the way to the tap, for everyone who depends on it.
Full detail: docs/ARCHITECTURE.md · Plain English: docs/CONCEPTS.md
Notes: Wrap-up. The scaffolding was the expensive part; the rest is filling it in.